## Slide 1: Real Time Scheduling Concepts
Girish S Kumar

## Slide 2: What is Scheduling policy/mechanism
A scheduling policy is a rule that selects the next running process
In a general purpose OS, it tries to balance the access to CPU, for all process hence a round robin kind of method suites well in case of general purpose OS
However in RTOS, the OS has to have control over the time so that each task completes the execution and produces the results with a specific time period. Hence the scheduling policy that is used in General purpose OS cannot be applied to RTOS directly

## Slide 3: Real Time Scheduling Methods
Clock Driven Approach
Weighted Round Robin Approach
Priority Driven approach

## Slide 4: State of process/task in RTOS
Executing
Ready to execute
Waiting
Preemeted
Got CPU
Needs Data
Get data
Needs Data
Get data

## Slide 5: Priority Driven Scheduling
In Priority Driven Scheduling, the CPU picks up the process with this highest priority
For this the CPU scans all the process in the “Tray” and selects the highest priority
P1
Priority-1
Exe time=10
P2
Priority-2
Exe time=30
P3
Priority-3
Exe time=20

## Slide 6: How does scheduling takes place
Process | Priority | Execution time | Release Time
P1 | 1 | 10 | T=0
P2 | 2 | 30 | T=15
P3 | 3 | 20 | T=18
Time | What does CPU do at this time slot
t=0 | P2 will run as it is the only task ready to run
t=15 | P1 is ready to run and it highest priority so it preempts P2 and run for 10 units of time
t=18 | P3 becomes ready but it has the lowest priority so it cannot preempt P1 or P2. So P1 will continue, till t=25 at the same timeP3 will be in waiting stage
t=25 | We have two process waiting for CPU, P2 and P3, P2 has higher priority than P3 so CPU will execute P2 till t=40,
t=40 | At this stage P1 and P2 is completed and no other task in the “tray” so P2 will start executing and completes by t=60
10
20
30
40
50
60
70
15
25
P2
P1
P2
P3

## Slide 7: How do RTOS set the priority of a Process/Task
We can set priorities in two ways either
Static : Which is also known as fixed priority system where the system designer set the priority of each task and it does not change with execution, this is very easy to design but its CPU utilization is not up to the mark
Dynamic : In this approach the priorities of the process changes with execution, design of this system needs more complex analysis on scheduling. This approach makes better use of CPU (better CPU utilization)

## Slide 8: Definitions
Process /Task for Encoding(compress)
Execution Time
Release time
Dead line
Audio Or video Sample ready
Sample has to be encoded
What is a periodic Task ?
A task which repeats its execution at a fixed frequency or period.
P(0)
P(1)
P(2)
P(3)
Period
Period
Period
Rate = 1/Period

## Slide 9: Scheduling Metrics
Ability to satisfy all dead lines
Scheduling overhead: The time required to make scheduling decision.
CPU Utilization – Is the percentage of time spend of executing a task/process, or doing useful work. Scheduling overhead is usually ignored which calculating this.
To calculate the CPU utilization for a period between t1 and t2 the formula is
U = Time Spend of useful work/ (t2-t1)

## Slide 10: CPU Utilizations
If the CPU Utilization is more that 100% the system won’t be stable. If the Utilization is less than on equal to 100% the system might work but stability is not guaranteed.
If the CPU utilization is less that 100% then system is expected to be stable. The CPU will have some spare bandwidth in this context to spare. This is kept as margin and marked as CPU bandwidth for “Idle” process.

## Slide 11
Hyper period
Hyper period is another parameter that is used to aspect in the scheduling metrices
How long is the time period we need to study to calculate the CPU utlization that is called the Hyper Period (Worst Case utilization). If look at the whole span of Hyper period it give us all the possible combinations of executions. So it helps us to evaluate a schedule
The concept of Hyperperiod applies to a scheduling system only if there are three or more task, it is a relative term used to understand the scheduling of periodic tasks.
To calculation of Hyperperiod of three periodic task is very easy, just take their period and find the Lowest common multiple of the three periods
Let us say we have three periodic task with Period 2, 5, 10, the lowest common multiple of three numbers is 20. From an analytical perspective we need a “Graph paper” which can mark 20 units of time to represent one cycle of execution of all the task..

## Slide 12: Example of Hyper period
Task Name | Period
P1 | 7 ms
P2 | 11ms
P3 | 15ms
LCM | 7 * 11* 15 = 1155ms
 | Hyper period = 1155 millisecond
Task Name | Period
P1 | 8 ms
P2 | 12 ms
P3 | 16 ms
LCM | 96 ms
 | Hyper period = 96 millisecond
Change the priority
a bit and see the
Change in hyper period
Smaller the hyper period better is the schedulability of the tasks.
Hyper period can be used for estimating the processor feasibility at the analysis stage

## Slide 13: Hyper period and CPU utilization
Process | Period | Execution time
P1 | 1 X 10-3 | 1 X 10-4
P2 | 1 X 10-3 | 2 X 10-4
P3 | 5 X 10-3 | 3 X 10-4
Let us say we have three process/tasks with the following parameters
To calculate the utilization, we have to figure out how many times each process is
executed in one hyperperiod: P1 and P2 are each executed five times while P3 is executed
once.
CPU Utilization = (5 X 10-4 + 5 X 10-4 + 1 X 10-4) / 5 X 10-3 = 0.22
Which is very much below 100% limit

## Slide 14: Rate Monotonic Scheduling
We discussed about two priority based scheduling algorithms. One is based on static priority and other is based on Dynamic priority
Rate Monotonic is a static priority scheduling method . It does not change the priority during execution
RMS model makes the following assumptions
Zero context switching time
Process executing time is constant, will not change with time
Activation time is at the beginning of the period
Dead line is always at the end of of the period
There are no assumptions on the relations ship between periods
There is only one CPU available for execution

## Slide 15: Rate Monotonic Scheduling
RMA is that a relatively simple scheduling policy
Priorities are assigned such that the process with the shortest
period being assign highest priority. This fixed-priority scheduling
policy is the optimum assignment of static priorities to processes,
in that it provides the highest CPU utilization
Response time is defined as the time require to finish the process even when all the interference from other process is taken into account. The critical instant for a process is defined as the instant during execution at which the task has the largest response time. It is easy to prove that the critical instant for any process P, under the RMA model,
occurs when it is ready and all higher-priority processes are also ready. We can use critical-instant analysis to determine whether there is any feasible
schedule for the system.

## Slide 16: RMS algorithm
/* -----------------------------------
processes[] is an array of process activation records,
stored in order of shortest peroid , with processes[0] being
the highest-priority process
-----------------------------------------*/
Activation_record processes[NPROCESSES];
void RMA(int current)
{
int i;
/* turn off current process (may be turned back on) */
processes[current].state = READY_STATE;
/* find process to start executing */
for (i 0; i < NPROCESSES; i)
{
if (processes[i].state READY_STATE)
{
/* make this the running process */
processes[i].state EXECUTING_STATE;
break;
}
}
}

## Slide 17: Rate Monotonic Scheduling case study
Process Name | Execution Time | Period
P1 | 3 | 20
P2 | 2 | 5
P3 | 3 | 10

## Slide 18: Rate Monotonic Priorities
Analysis of RM lead to the following facts
For a fixed priority assignments
Shortest period get the highest priority
Priority is inversely proportional to the period
Breaks ties arbitrarily
This approach depends only the period
NO other fixed priority method works better than RMS

## Slide 19: CPU Utilization in RMS
For arbitrary dead line the critical instances does not always happen
Critical instance always happen when all the process are ready to run, that happens very rare not all the time. Schedule has to be designed to account for this worst case
One solution when such a case happens is to use the idle time of CPU
RMS does not guarantee 100% utilization of CPU however some combinations do

## Slide 20: Asymptotic analysis of RMS
Asymptotic analysis allow us to analyze an algorithm behavior or running time by analyzing its input size.
CPU Utilization = Sum (Sigma) of the ratios of all process (Computation time/period)
As we increase the number of processes to infinity with no restriction on period we can mathematically prove that the CPU utilization is 69% (max)
This asymptotic analysis proves that RMS does not give 100% CPU Utilization
However it guarantees meeting 100% dead lines

## Slide 21: Earliest-Deadline-First Scheduling
Earliest deadline first (EDF) is another well-known scheduling policy
It is a dynamic priority scheme—it changes process priorities during execution based on initiation times.
It can achieve higher CPU utilizations than RMS.
It assigns priorities in order of deadline. The highest-priority process is the one whose deadline is nearest in time.
the lowest priority process is the one whose deadline is farthest away.
Priorities must be recalculated at every completion of a process.
However, the final step of the OS during the scheduling procedure is the same as for RMS—the highest-priority ready process is chosen for execution.

## Slide 22: EDF Algorithm
For each unit of time
{
For every process
{
Find the processes which are ready to execute
Pick up the process whose dead line is closest
execute the process
}
}

## Slide 23: Case study of EDF
Process Name | Execution Time | Dead line | Period
P1 | 3 | 7 | 20
P2 | 2 | 4 | 5
P3 | 3 | 8 | 10

## Slide 24: EDF vs RM which is better
EDF can extract higher utilization out of the CPU, but it may be difficult to
diagnose the possibility of an imminent overload. Because the scheduler
does take some overhead to make scheduling decisions, a factor that is ignored in
the analysis of both EDF and RMS,running a scheduler at very high
utilizations is somewhat problematic.
RMS achieves lower CPU utilization but is easier to ensure that all deadlines
In some applications, it may be acceptable for some processes to
occasionally miss deadlines. For example, a set-top box for video decoding is not
a safety-critical application, and the occasional display artifacts caused by missing
deadlines may be acceptable

## Slide 25: What if your set of processes is un-schedulable ?
Get a faster CPU. That will reduce execution times without changing the periods, giving you lower utilization. This will require you to redesign the hardware, but this is often feasible because you are rarely using the fastest CPU available.
Redesign the processes to take less execution time. This requires knowledge of the code and may or may not be possible.
Rewrite the specification to change the deadlines. This is unlikely to be feasible, but may be in a few cases where some of the deadlines were initially made tighter than necessary.

## Slide 26: Assumptions behind modeling
Each process is totally self contained, that is not always the case
Example
a process may need a system resource, such as an I/O device or the bus, to complete its work. Scheduling the processes without considering the resources those processes require can cause priority inversion, in which a low-priority process blocks execution of a higher priority process by keeping hold of its resource.

## Slide 27: Priority Inversion
Priority inversion
Consider a system with two processes: the higher-priority P1 and the lower-priority P2. Each uses the microprocessor bus to communicate to peripherals. When P2 executes, it requests the bus from the operating system and receives it. If P1 becomes ready while P2 is using the bus, the OS will preempt P2 for P1, leaving P2 with control of the bus. When P1 requests the bus, it will be denied the bus, since P2 already owns it. Unless P1 has a way to take the bus from P2, the two processes may deadlock.

## Slide 28: Priority Inversion
The most common method for dealing with priority inversion is to promote the priority of any process when it requests a resource from the OS. The priority of the process temporarily becomes higher than that of any other process that may use the resource. This ensures that the process will continue executing once it has the resource so that it can finish its work with the resource, return it to the OS, and allow other processes to use it. Once the process is finished with the resource, its priority is demoted to its normal value. Several methods have been developed to manage the priority swapping process Rate-monotonic scheduling assumes that there are no data dependencies between processes.

## Slide 29: Data dependencies and scheduling
Data dependencies imply that certain combinations of processes can never occur.
P1
P2
P3
P1 | CPU Time
P1 | 2
P2 | 1
P3 | 4
We know that P1 and P2 cannot execute at the same time, since P1 must finish before P2 can begin. Furthermore, we also know that because P3 has a higher priority, it will not
preempt both P1 and P2 in a single iteration. If P3 preempts P1, then P3 will complete before P2 begins; if P3 preempts P2, then it will not interfere with P1 in that iteration. Because we know that some combinations of process cannot be ready at the same time, we know that
our worst-case CPU requirements are less than would be required if all processes could be
ready simultaneously.

## Slide 30: Interrupt handling

## Slide 31
Clock Driven Scheduling periodic tasks
Clock Driven Scheduling of periodic + aperiodic task
Clock Driven Scheduling of periodic + aperiodic task + Sporadic Tasks
Priority Driven Scheduling periodic tasks
Priority Driven Scheduling of periodic + aperiodic task
Priority Driven Scheduling of periodic + aperiodic task + Sporadic Tasks