## Slide 1: Real Time Scheduling Concepts
Girish S Kumar

## Slide 2: Real Time Scheduling Methods
Clock Driven Approach
Weighted Round Robin Approach
Priority Driven approach

## Slide 3: Clock Driven Approach
This is also called Time Driven Scheduling
This is usually used in Hard Real time System
Where all the parameters of the job are known to the designer in advance
The designer prepares a “Time Table” of what jobs has to be executed at a for a given slot and hard wired into the system. The system based on the “Time Table” each job is executed. In this case the scheduler as such does not have much of over head to other than just triggering the task based on the “Time Table”.
Usually a hardware timer is used to implement a clock driven approach.
In this case the designer is pretty well aware of the start time and finish time of each job in advance,
This approach works well when the execution time of a job (time gap between start time and end time of a job) it pretty my stable to very well know. The variance between two successful execution of a given job will be negligible

## Slide 4: Examples
Robotics
Satellites
On Board Diagnostics
Delivery Drones
Emergency Services
Unmanned Submarines

## Slide 5: Weighted Round Robin Approach
For high speed switches/ routers which handles large amount of data Traffic needs special kind of Scheduling Algorithm. This is a modification of Traditional Round Robin scheduling, where every process is giving a fixed time slot to execute.
In case of Weighted Round Robin scheduling instead of giving the same priority for every a job, each job is giving different weight , so that fraction of the process time available for each job will be different for based on the need.

## Slide 6: Priority Driven Approach
In this method every task is giving a priority and tasks are executed based on priority
As List of jobs are maintained by the Operating system.
As long as there are jobs in the list the CPU will never go into Idle mode with this approach
This is not always the best for Real time applications but there are cases where this approach is used in embedded applications
P1
P2
P3
J1
J2
J3
J4
J5
Jn
List

## Slide 7: Static Binding to processors
In this method the list of Jobs are partitioned into separate lists and each list is assigned to a processor statically
If any job is depended on another in a different queue, schedulers take care of that,
P1
P2
P3
J13
J13
J7
J8
J10
Jn
List
J5
J2
J6
J4
J5
Jn
J11
J12
J9
J14
J15
Jn

## Slide 8: EDF and LRT
EDF Stands for Earliest Dead Line First Algorithm. Dead Line of a Job mean the time by which the job/task has to be completed.
EDF is a way to assign priority to jobs based on the deadlines, in this case, the jobs with Earliest Dead Line is given the highest priority
Release time is the time by which a Job is ready for execution/scheduling. Another way to schedule jobs is based on Release Time .The Latest Release time (LRT) which is the reverse of EDF treats release times as dead line and dead lines as releases and schedules jobs.

## Slide 9: Clock Driven vs Priority-Driven
No | Clock Driven | Priority Driven
1 | Need to know the Release time,execution time and deadline of each job at the design time | Easy to implement – Just know the priority of each job
2 | Not suitable for application with varying time and resource requirements | Suitable for applications which with varying time and resource requirements
3 | Used widely in Hard Real time system | Not suitable for hard real time systems
4 | Timing behavior is deterministic | Timing Behavior is non deterministic

## Slide 10: Clock Driven Scheduling A closer Look

## Slide 11
Real Time System
Async I/P
Periodic
Inputs from
Sensors
(Push)
Output
Reference Model
Periodic
Polling of sensors
(Pull)

## Slide 12: Notations for Clock Driven Scheduling
Notation | Meaning
Ti | A periodic task with number ‘i’
Release Time Di | Release time is the time by which a Job is ready for execution/scheduling
Dead Line Di | Dead Line of a Job mean the time by which the job/task has to be completed.
pi | The period of task Ti is the minimum length of all time intervals between the release time of two consecutive jobs in task Ti
ei | The execution time of the period task Ti
Job Jn | A Task Ti can be considered of J1, J2….. Jn and Ti implemented as system function

## Slide 13: Notations for Clock Driven Scheduling
Notation | Meaning
Phase of Ti fi | Is the Release time of the first Job J1, in Task Ti Tasks which has the same means – The first job has the same release time, of the first job in their list is ready for execution at the same time
H Hyper period | Let us say we have a periodic task Ti with period pi . Now we have n such task 1,2,3…..n. Let us take the Least Common Multiple of periods all the n task ie the LCM of values P1 , P2 , P3 ….. Pn - This value is called the Hyper period (H) of the period tasks
Ui | The utilization of Task Ti is the ratio of execution time ei with period pi ie U I = ei/pi

## Slide 14: Clock Driven scheduler
Input Stored scheduled Table of tasks Tk For k = 0,1,…….. N -1
TASK Scheduler
Set the next decision point i to the table entry k = 0
Set the timer to expire at tk - tk is the time at which this task has to be scheduled
Do Forever:
accept timer interrupt
if an aperiodic job is executing currently, preempt the job
Current Task T = Tk
increment i by one ( i = i + 1)
compute the next table entry k = I mod (N)
set the timer to expire at [i/N] * H + tk
if the current task T is idle task
let the job at head of the aperiodic job queue execute
else
let the task T execute
sleep
end SCHEDULER

## Slide 15: Clock Driven scheduler improved
In the previous scheduling method , the scheduling decision was made in adhoc manner
(Each time the interrupt is set),
A better organized approach would be to make scheduling decision periodically (rather than controlled by interrupts)
For this the time line is divided into equal time intervals called Frames, every frame has a length f called its frame size, scheduling decision is made at the beginning of each frame. In other word the first job of every task is released at the beginning of some frame.
In addition to executing the job, we want scheduler to carry out monitoring actions at the beginning of each frame . Scheduler should check
Every job scheduled in the frame has been released and ready for execution
Every job is completes within the deadline
So every some CPU time need to allocated to scheduler to do the monitoring activities listed above

## Slide 16: What should be length of each frame
A frame should be sufficiently large enough to so that every job can start and complete within the frame. To meet this criteria we can select frame length f
f >= max(ei) f >= max(execution time)
t
t + f
t + 2f
t + 3f
General Structure of a cyclic scheduler

## Slide 17: What if the a job spread across multiple frames
When a job is spread across multiple frame calculation of the frame size is slightly different
Note : within a Frame we need some CPU bandwidth to do book keeping like monitoring whether is job is released on time and completed before or at the dead line
There should be atleast one frame between the release time and deadline of every job
frame k
frame k + 1
frame k + 2
t + f
t + 2f
t + 3f
t
t`
t` + Di
Release time
Deadline
2f – gcd(pi ,f) <= Di

## Slide 18: Disadvantages with this approach
It is always possible to design tasks and job so that it fit within the constraints discussed
So it jobs with large execution time need to cut into slices with smaller execution time
Based on this we need to
Choose a frame size
Cut jobs into smaller slices
Placing the jobs in frames
The more the number of job slices higher context switch and over heads. If we cut the job into fewer slices it may not meet the frame constraints
Handling aperiodic jobs becomes a challenge

## Slide 19: Cyclic Executives
Cyclic executive is more of a c table driven cyclic scheduler for all type of jobs in a multithreaded system. Scheduling decisions are made only at the beginning of each frame It allows aperiodic and sporadic jobs to use the time not used by periodic tasks
The cyclic executive takes over the processor and executes at each of the clock interrupts which occur at the beginning of frames. When it executes , the cyclic executive copies the table entry for the current frame into the current block. It then wakes up a job, clled the periodic task server and let the server execute the job slices in the current block. Upon the completion of periodic task server, the cyclic executive wakes up the a-periodic jobs in the corresponding job queue in turn and allows them to use the remaining time in the frame.

## Slide 20: Cyclic Executive Algorithm
Input : Stored Schedule L(k) for k = 0,1,….. F-1
Aperiodic Job Queue
Task CYCLIC EXECUTIVE:
The current time t = 0;
The Current frame k = 0
Do forever
Accept clock interrup at time tf ;
currentBlock = L(k)
t = t + 1
k = t mod F ;
if the last job is not completed, take appropriate action;
wake up the periodic task server to execute the slices in currentBlock
sleep until the periodic task server completes
while the aperiodic job queue is non empty
wake up the job at the head of the aperiodic job queue
sleep until the aperiodic job completes
remove the aperiodic job from the queue
endwhile
sleep intil the next clock interrupt;
enddo;
End CYCLIC_EXECUTIVE

## Slide 21: Response time of Aperiodic jobs
aperiodic jobs, are scheduled in the background after all the job slices with hard deadlines are completed.
Since aperiodic jobs are released and executed by the system in response to an event, the sooner the aperiodic job completes, more responsive the system is. For this reason minimizing the reponse time of each a periodic job or the average response time of all the aperiodic jobs is typically one of the desing goals of real time schedulers
Aperiodic jobs are those jobs released at random time instances.Aperiodic jobs has either soft deadlines or no deadlines.

## Slide 22: Slack Stealing – A method for scheduling aperiodic jobs
One approach to way to improve the response times of aperiodic jobs is by executing the aperiodic jobs ahead of the periodic jobs whenever possible. This approach, called slack stealing,
For the slack-stealing scheme described below to work, every periodic job slice must be scheduled in a frame that ends no later than its deadline.
Let the total amount of time allocated to all the slices scheduled in the frame k be xk The slack (time) available in the frame is equal to f − x(k) at the beginning
of the frame. If the aperiodic job queue is nonempty at this time, the cyclic executive can let aperiodic jobs execute for this amount of time without causing any job to miss its deadline. −
K-th frame
K + 1 th frame
X(k)
Time given for scheduled task
f
f- x(k)
f - x(k) – t > 0
For aperiodic task to execute where
T is the amount of slack time utilized so far.

## Slide 23: Average Response time
Aperiodic task do not have hard dead lines, how they need to be completed and we need to track of the how fast the aperiodic task was completed, to avoid any chance of getting “trapped” and getting “aged” in the system.
For this the designer focus on a measurement called “ Average Response Time” for aperiodic task, this gives an indication of how fast the aperiordic job was completed. During the design phase of a RT designers need to give a promise of the his measurement “Average Response time”
Since average response time is a statistical measurement, designers apply the principle of queuing theory to arrive at a estimate of this value.
Real Time System
4
3
2
1
Queue of aperiodic tasks

## Slide 24
Let us assume we ‘n’ aperiodic jobs at a given point of times, as they are aperiodic
Tasks keep arriving at the queue at different rates (no of task arriving per sec) at
This value of R will keep changing every sec or every unit of time. So for every second
Or every unit of time we have a different value of R which can noted as
R1, R2, R3, …. R(i) corresponding to each task (i) per unit time
Let us take the i-th task
Just like each task has arrival time, the time at which it arrived there is a execution time
The time it took to execute the job Let it be E[B(i)] for the i-th task. This is actually random value and varies from job to job
Since we are working with random variables, we need to apply the principles of queuing theory we get the Average response time of aperiodic task is

## Slide 25
SUM of i = 1 to n [R(i) E[B(i)] +
R(1- U)
W0
(1-U)2 1 - UA/(1 – U)
W0 = SUM of i = 1 to n [R(i) E[B(i)2]
2
UA is the total average utilization of aperiodic tasks;
U is the total utilization of all the periodic tasks

## Slide 26: Scheduling of SPORADIC jobs
Sporadic jobs are those jobs released at random time instances. Sporadic jobs has hard deadline.
As soon as sporadic job arrives , the scheduler checks whether the newly released sporadic job can be feasibly scheduled with all the jobs in the system at the time.
If according to the existing schedule, there is a sufficient amount of time in the frames before its deadline to complete the newly released sporadic job without causing any job in the system to complete too late, the scheduler accepts and schedules the job.
Otherwise, the scheduler rejects the new sporadic job. By rejecting a sporadic job that cannot be scheduled to complete in time immediately after the job is released, the scheduler gives the application system as much time as there is to take any necessary recovery action.
Conveyor belt carrying assembled parts and robotic ARM removing the defective piece
before it gets into packing stage. The job of robotic ARM to remove the part is a sporadic
Job.

## Slide 27: Scheduler
EDF algorithm is a good way to schedule accepted sporadic jobs.
For this purpose, the scheduler maintains a queue of accepted
sporadic jobs in non decreasing order of their deadlines and inserts
each newly accepted sporadic job into this queue in this order.
Whenever all the slices of periodic tasks scheduled in each frame are
completed, the cyclic executive lets the jobs in the sporadic job queue
execute in the order they appear

## Slide 29: What Kind of scheduler does VxWorks Uses ?
Vxworks has two major scheduling algorithms such as priority scheduling and round round-robin scheduling.
Priority scheduling
In priority scheduling gives a priority to each process (thread). The highest priority thread is
to be executed first and so on. The same priority processes are executed on a first come
first serve basis. Priority can be decided based on time requirement, memory requirement
or any other resource requirement.
Round-Robin Scheduling
Round-Robin is the scheduling algorithm used by the CPU during execution of the process.
It is specially designed for time sharing systems. In round-robin scheduling assigned a
fixed time to each process. Mean once a process is executed in a given time period then
other process is permitted to execute for a given time period. The round robin scheduling is
better in real time operating system.
Interrupts
To achieve the fastest possible response to external interrupts, interrupt service routines
in Vx works run in a special context outside of any process context, so that there is no process
context switches involved. The ISR address is stored in the interrupt vector table and is called directly
from the hardware. The ISR initially performs some work (eg. Saving registers and setting up stack) and
then calls the C functions that was attached by the user.

## Slide 30
Clock Driven Scheduling periodic tasks
Clock Driven Scheduling of periodic + aperiodic task
Clock Driven Scheduling of periodic + aperiodic task + Sporadic Tasks
Priority Driven Scheduling periodic tasks
Priority Driven Scheduling of periodic + aperiodic task
Priority Driven Scheduling of periodic + aperiodic task + Sporadic Tasks